Quick setup guide:		CMX88

Example system (only using 4 inputs, CMX88 supports up to 8 inputs and outputs):

Sources:

1. Cable box with component & composite video, analog audio, and digital audio coax out

2. Xbox with component video, analog audio, and digital audio optical out

3. DVD with component & composite video, analog audio, and digital audio optical out

4. PVR with component & composite video, analog audio, and digital audio optical out

Displays:

1. Projector (living room) with component video in

Receiver (living room) with analog audio and digital audio optical in

2. Plasma (bed room) with component video in and analog audio in

Receiver (bed room) with analog audio and digital audio coax in

3. RPTV (game room) with component video in and analog audio in

Receiver (game room) with analog audio and digital audio coax in

4. LCD (kitchen) with component video in and analog audio in

5. CRT (garage) with composite video in and analog audio in

6. Built in wall speakers (bedroom)

Step 1:  Plan your system

What we are trying to accomplish is a full featured 5 zone viewing environment.  We will be able to watch any of the 4 sources on each display.  Since CMX88 is a matrix switch, we can display the same source to both viewing areas or different sources.

For audio, we will be sending analog audio and digital optical to the living room.  Analog audio and digital optical will be sent to the bed room and game room.  We are sending both analog audio and digital audio so we can use the tv speakers only if we do not want to turn on the receiver.  For the kitchen, we will send analog audio only since we don’t have a receiver.  CMX88 will transcode between digital audio coax and optical, so we can use coax in the bedroom and game room since it is a less expensive long cable.  We will use optical in the living room, but could switch to coax if our needs change.  For the garage we will send composite video and analog audio.  The bedroom has built in wall speakers.  We will send analog audio to that zone and be able to control the volume with the CMX88 switch.

For simplicity, we will use the basic mode => audio and video for each output switch together.  If in the future we decide that we would like to control the audio and video separately, we can always change to advanced mode.

For control, we will use both the front panel buttons and the IR remote.  If we had a fully programmable remote like the Pronto, we could use the default IR codes and just load the config file into the Pronto.  Here we do not have a Pronto, so we will use the Zerokey IR learning function of the CMX88 with our basic remote.

Once all the cables are in place, we are ready to install the CMX88

Step 2:  Connecting CMX88

Make sure all the equipment is unplugged.  See the figure on the last page for illustration.

Remember, all CMX88 inputs are on the LEFT side when looking at the back!

Cable box:

- Connect the component video cable from the red/green/blue rca jacks on the cable box to the red/green/blue input jack on CMX88 labeled “1”

- Connect the composite video cable from the yellow jack on the cable box to the yellow composite video input jack on CMX88 labeled “1”

- Connect the analog audio cable from the red/white rca jacks on the cable box to the red/white input jack on CMX88 labeled “1”

- Connect the digital audio cable from the correct rca jack on the cable box to the yellow digital audio input jack on CMX88 labeled “1”

Xbox:

- Connect the component video cable from the red/green/blue rca jacks on the Xbox hd output adapter to the red/green/blue input jack on CMX88 labeled “2”

- Connect the analog audio cable from the red/white rca jacks on the Xbox hd output adapter to the red/white input jacks on CMX88 labeled “2”

- Connect the toslink cable from the toslink jack on the Xbox hd output adapter to the toslink input jack on CMX88 labeled “2”

DVD:

- Connect like Xbox using the CMX88 input jacks labeled “3”.

- Connect the composite video cable from the yellow jack on the DVD to the yellow composite video input jack on CMX88 labeled “3”

PVR:

- Connect like DVD using the CMX88 input jacks labeled “4”.

Remember, all CMX88 outputs are on the RIGHT side when looking at the back!

Projector:

- Connect the component video cable from the red/green/blue rca jacks on the projector to the red/green/blue output jack on CMX88 labeled “1”

Receiver (living room):

- Connect the toslink cable from the toslink jack on the receiver to the toslink output jack on CMX88 labeled “1”

Plasma:

- Connect the component video cable from the red/green/blue rca jacks on the plasma to the red/green/blue output jacks on CMX88 labeled “2”

- Connect the analog audio cable from the red/white rca jacks on the plasma to the red/white output jacks on CMX88 labeled “2”

Receiver (bed room):

- Connect the digital audio cable from the correct rca jack on the receiver to the yellow digital audio output jack on CMX88 labeled “2”

RPTV:

- Connect the component video cable from the red/green/blue rca jacks on the RPTV to the red/green/blue output jacks on CMX88 labeled “3”.

- Connect the analog audio cable from the red/white rca jacks on the RPTV to the red/white output jacks on CMX88 labeled “3”.

Receiver (game room):

- Connect the digital audio cable from the correct rca jack on the receiver to the yellow digital audio output jack on CMX88 labeled “3”.

LCD:

- Connect the component video cable from the red/green/blue rca jacks on the LCD to the red/green/blue output jacks on CMX88 labeled “4”.

- Connect the analog audio cable from the red/white rca jacks on the LCD to the red/white output jacks on CMX88 labeled “4”.

CRT:

- Connect the composite video cable from the yellow rca jack on the CRT to the yellow composite video output jack on CMX88 labeled “5”.

- Connect the analog audio cable from the red/white rca jacks on the CRT to the red/white output jacks on CMX88 labeled “5”.

Speakers:

- Connect the analog audio cable from the red/white rca jacks on the speakers to the red/white output jacks on CMX88 labeled “6”.

Step 3:  Configuring the mode

Plug in the CMX88 and press on of the front buttons to power it on

(Note basic mode is the factory default, so this step is only shown for example)

Toggle the left button until “CF” (Config) is displayed on the left LED

Toggle the right button until “UF” or “UO” (basic or advanced mode) is displayed on the right LED

If “UO” (advanced scheme) is displayed, press and hold the right button for 6 seconds

The LED should now show “UF”, verifying you are in basic mode

Note:  You could instead select “C” on the right LED and then press and hold the right button for 6 seconds.  This would set CMX88 back to factory defaults, which is basic mode.

Step 4:  Controlling CMX88 via the front panel buttons

The left button will select which output you are controlling or config mode.  The left button display is the left LED.

“U1” : Output 1 is selected, the right LED will now show the current input for output 1

“U2” : Output 2 is selected, the right LED will now show the current input for output 2

“U3” : Output 3 is selected, the right LED will now show the current input for output 3

“U4” : Output 4 is selected, the right LED will now show the current input for output 4

“U5” : Output 5 is selected, the right LED will now show the current input for output 5

“U6” : Output 6 is selected, the right LED will now show the current input for output 6

“U7-8” : Output 5-8 selections.  We do not need these.

“G1-5”:  Analog audio gain control on outputs 1-5.  We do not need these.

“G6”:  Analog audio gain control on outputs 6.  Right displays the volume setting(0-15)

“G7-8”:  Analog audio gain control on outputs 7-8.  We do not need these.

“CF” : Config mode, the right LED will now show various config controls

The right button will toggle the right LED.  Use this button to select the input which will be connected to the current output.  The right LED will toggle through “C1-C8”, and then “O1-O8”.  When “O” is displayed, the digital audio optical jack input is being transcoded to both digital audio out coax & optical.  When “C” is displayed, the digital audio coax jack input is being transcoded to both digital audio out coax & optical.

Selecting DVD to living room projector & receiver:

Toggle left button until the left led shows “U1”

Toggle right button until the right led shows “O3”

Selecting DVD to bed room plasma & receiver:

Toggle left button until the left led shows “U2”

Toggle right button until the right led shows “O3”

Selecting Cable box to bed room plasma & receiver:

Toggle left button until the left led shows “U2”

Toggle right button until the right led shows “C1”

Selecting Cable box to game room RPTV & receiver:

Toggle left button until the left led shows “U3”

Toggle right button until the right led shows “C1”

Selecting Xbox to kitchen LCD:

Toggle left button until the left led shows “U4”

Toggle right button until the right led shows “O2”

Selecting Xbox to bedroom speakers:

Toggle left button until the left led shows “U5”

Toggle right button until the right led shows “O2”

Toggle left button until the left led shows “G5”

Right button controls volume, 0 is mute and 15 is max

Step 5:  Using ZeroKey IR learning for remote control

Please read the IR control section of the manual before programming the IR control.

The IR interface of the CMX88 uses a three code command sequence.  For this installation, we will need to program the following codes:

Output type select codes:  “U”, “G”  = IR code 0,6

Output select codes:  1-6 = IR codes 8-13

Input select codes: C1,O2,O3,O4,Volup,Voldwn  = IR codes 25,34,35,36,40,41

To control the CMX88, we can to map each of these discreet codes to a separate key on our remote.  In total we need 14 unique keys.

We are going to start by finding our receiver universal remote.  Like most universal remotes, it can control several devices.  In our system, we don’t have a VCR so we are going to use those codes to control CMX84.

Remote (VCR selected) key Play =>  AV switch select = code 0

Remote (VCR selected) key Stop =>  Volume select = code 6

Remote (VCR selected) key 1 => output select 1 (projector) = code 8

Remote (VCR selected) key 2 => output select 2 (plasma) = code 9

Remote (VCR selected) key 3 => output select 3 (RPTV) = code 10

Remote (VCR selected) key 4 => output select 4 (LCD) = code 11

Remote (VCR selected) key 5 => output select 5 (CRT) = code 12

Remote (VCR selected) key 6 => output select 6 (Bedroom) = code 13

Remote (VCR selected) key 7 => input select 1C (cable) = code 25

Remote (VCR selected) key 8 => input select 2O (xbox) = code 34

Remote (VCR selected) key 9 => input select 3O (dvd) = code 35

Remote (VCR selected) key 0 => input select 4O (pvr) = code 36

Remote (VCR selected) key RV => Volume up = code 40

Remote (VCR selected) key FF => Volume down = code 41

The IR control codes numbers on the far right were taken from the IR code table in the manual.

For each of these remote keys, we need to program the CMX88 to learn the transmitted code.  Keep in mind it is the CMX88 that is doing the recording, so don’t try to put the remote in “learn” mode.  Here are the steps for each key:

For each key:

Toggle the left front panel button until “SZ” is displayed

Toggle the right front panel button until the number matches the IR control code you wish to program (see above table)

Press and hold the right front panel button for 6 seconds

Release the left front panel button

The right LED should now be flashing, it is ready to record

Press the correct key on the remote (see above table)

The left LED should stop flashing, this key is stored

The CMX88 may switch at this time depending on the code

Example:  To record Vol UP control:

Toggle the left front panel button until “SZ” is displayed

Toggle the right front panel button until the number “40” shows

Press and hold the right front panel button for 6 seconds

Release the left front panel button

The right LED should now be flashing, it is ready to record

Press the RV key on the remote

The left LED should stop flashing, this key is stored

After storing all 14 remote keys, you can now control CMX88 with that remote.

Selecting DVD to projector:

Make sure universal remote is on “VCR” setting

Press remote button “Play”  (select AV switching)

Press remote button 1  (select projector)

Press remote button 9  (select DVD)

Selecting Cable box to plasma:

Make sure universal remote is on “VCR” setting

Press remote button “Play”  (select AV switching)

Press remote button 2  (select plasma)

Press remote button 7  (select Cable)

Controlling volume in Bedroom:

Make sure universal remote is on “VCR” setting

Press remote button “Stop”  (select Volume control)

Press remote button 6  (select bedroom)

Press remote button “RV”  (volume up)

Press remote button “FF”  (volume down)

If you ever need to change remotes, you can use the config clear command (“CFC” on LED and hold right button for 6 seconds) to reset all the codes at once.

This completes installation and setup of the CMX88.  If you have further questions please check our FAQ forum at video-storm.com for the most recent information.

Rear panel diagram :