CRM88 Video Switch input termination jumpers

Jumper Setting Guide

Setting the input termination jumpers on the CRM88 video switch is approximately the same level of difficulty as installing an expansion board in a PC.  You will need the following equipment for the installation.  Video Storm LLC is not responsible for any damage resulting from improper end user reassembly of this product.  If you do not have the proper equipment or do not feel confident with the procedure, please contact support@video-storm.com and arrange for the jumper to be modified at the factory.

Required equipment:

- ESD safe (static free) work area including personal ESD static dissipative device

- Philips screwdriver

It is very important that you disconnect POWER and ALL external cables from the CRM88 switch before beginning.  Do not open the case when the device is powered OR connected to any other cables.

NOTE: If any ribbon cables become loose during disassembly or reassembly, please make sure they are not reinserted with the wrong orientation, as this will damage the unit. If you are not sure which way to insert ribbon cables, please contact support.

Please read through all the steps below prior to starting.  If you have any questions, please contact support@video-storm.com.

- Remove the front panel

  - Locate the six screws on the front panel (pictured).  Remove these screws.

  - Lay the front panel down while leaving the ribbon cables attached as shown.  Do not remove the ribbon cables.

- Remove the cover screws from the back panel

  - Locate the three screws on the rear panel that secure the top cover (pictured).  Remove these screws.

- Remove the cover screws from the right and left sides

  - Locate the two screws on each side (4 total).  Remove these screws.  If you have the rack ears attached you must remove these first.

- Remove the top cover

  - While facing the rear panel, hold the top cover from both sides and slide back about 1 inch and pick up.  The top cover should be removed in this fashion.  This can be a bit tricky so you may need to try several times.  The screw taps on the cover may catch on the rca boards so be careful not to force these.

  - Place the top cover aside.

- Locate the jumpers

  - The 4 jumpers are circled in the picture.  They are also labeled SHUNT1 – SHUNT4 on the circuit board.  In the picture we have removed the cables for clarity.  Do not remove any cables when changing the jumpers.

Note, the picture shows 8x8 mode (Shunt 1, 2 IN, Shunt 3, 4 OPEN)

- Set the jumpers for the desired mode

  - When the jumpers are inserted, that input bank will have 75 ohm input termination.  When the jumper is open, or inserted on 1 side of the pins only, that input bank will have 10K ohm input termination.

  - Set the jumpers for the desired mode according to the table.  When the jumpers are “open”, it is best to leave them connected to one side of the pin bank so they will not get lost.

| Mode | SHUNT1 | SHUNT2 | SHUNT3 | SHUNT4 |
| --- | --- | --- | --- | --- |
| 8x8 | In | In | Open | Open |
| 16x16 component video | In | In | In | In |
| 16x16 composite / analog audio | Open | Open | Open | Open |

- Re-attach the top cover

  - Flip the top cover back over and re-attach to the CRM switch.

  - The top cover is installed by first aligning the right side when the cover is about 1 inch away from the back panel.  Then align the left side and slide the cover all the way to meet the back panel.  This can also be quite tricky and require several tries to get to perfect.  Once again make sure the rear screw taps do not get caught on the CRM boards.

  - The cover is properly in place when the screw holes line up. If the screw holes do not align, you need to re-attach the cover again. Do not force screws into the holes.

- Insert the Rear panel screws (3)

- Insert the side panel screws (4 total)

- Reattach the front panel

  - Hold the front panel up to the front of the CRM switch.

  - When the screw holes are aligned, insert the top 2 screws firsts.  After these insert the remaining 4 screws.

- Finally check to make sure all screws are attached

- Power up check

  - Plug in the DC power cable

  - Press the front left button

  - If the LED does not come on, the reassembly was done incorrectly.  Immediately disconnect the DC power cable and contact support@video-storm.com.

  - If the LED is normal, then you are done.