Model CSW62

Ultra Wide bandwidth HDTV

integrated switch & distribution amplifier

Overview:

This product integrates a professional grade component video switch with an ultra wide bandwidth distribution amplifier.  The most common application for this device is shown below.

Switching 6 sets of component video to 2 displays or storage devices

The CSW62 can also support the following applications

- Switching 6 sets digital audio + composite video to 2 receivers

- Switching 6 sets HDTV + digital audio to 2 inputs of certain TVs to support both 480i & hdtv  (useful with xbox)

The CSW62 is the optimal solution for all these applications because it is built with the best high performance video amplifiers.  The specs speak for themselves; this unit delivers ultra clean noise performance and more bandwidth than needed for all high definition video standards.  The CSW62 is also the easiest component switch on the market to setup and use.  Our proprietary ZeroKey technology allows our device to be controlled by any key on any remote.  No need for separate remotes or remote programming.

CSW62 also integrates an active DC restoration circuit.  This circuit restores the DC levels of the output video to the correct specifications regardless of what they are on the input.  This is particularly useful for certain projectors and monitors that do not support out of spec DC levels.  It will also eliminate any changes in brightness during rapid scene changes.

All existing analog video formats including HDTV can be handled by this amplifier.

Unit includes

- CSW62 component switch & distribution amplifier as pictured

- 16 inputs, 8 outputs  (Inputs: 6 switched sets of 3; Outputs: 2 sets of 3)

- 9V wall power supply

- 3 year parts and labor warranty

Installation

Please use the following steps to install and setup your CSW62.  If you have any questions, contact your retailer or visit www.video-storm.com for help.

- Connect the video inputs and outputs.  For component video, match the cable colors to the red/green/blue video inputs & outputs.  For composite video, you may use any set.

- Connect the supplied wall transformer to a properly grounded power outlet.  Plug into DC input of the CSW62, you should see the LED light on the front panel.

Programming the ZeroKey remote interface

The remote control interface uses ZeroKey infrared code cloning to map any remote control key to each one of the four inputs.  Here are the steps to program the CSW62 for your remote.

- Press the toggle button to select the input you would like to train

- Hold the toggle button for 6 seconds and release

- The LED indicator for the selected channel will now flash continuously, this means it is ready to be programmed

- Aim your remote control at the CSW62 and press the key you would like to use to select this input

- The LED indicator will stop flashing, this means the code has been stored.

- Repeat for the other  inputs

ZeroKey technology is compatible with virtually all remote controls, and does not interfere with the normal operation of the remote.  The best way to use this is to program the CSW62 with the same keys you normally push to switch your AV receiver or TV.  The CSW62 will switch at the same time as your TV or receiver without the need for complicated macros or pushing extra buttons!

ZeroKey programming is stored in flash memory, and you will not need to reprogram even if you lose power.  If you buy a new remote in the future, don't worry, the CSW62 can be reprogrammed as much as you like.

Specifications

- 18 inputs
    75Ohm terminated at all frequencies 
    Gold plated matched low impedance RCA jacks
    1Vpp nominal input swing (Ypbpr) or 1.3Vpp (Cvbs)   2.5Vpp maximum   
    Crosstalk < -80 dB

- 6 outputs   
    Source impedance 75 Ohms
    Gold plated matched low impedance RCA jacks
    DC restored for maximum compatibility
    High performance amplifier capable of driving over 100ft of coax per output
    Noise spectrum > 60 dB
    -3dB bandwidth > 100 Mhz

- Internal design 
    Flash programmable micro controller enables ZeroKey remote technology
    Ultra wide bandwidth t-switches prevent crosstalk or signal distortion
    High performance video amplifiers for best performance
    High reliability capacitors and self resetting fuse protection for long life

- Housing 
    Black powder coat aluminum housing   8.25" x 4.25" x 2.5"

LED indicators

The LEDs on the front panel of CSW62 indicate which input is currently selected.  The 3 LEDs are binary encoded to represent the 6 available inputs.  The following table shows how they should be interpreted.  You can also just add the numbers of the LEDs that are on to get the selected input.

| LED 1 | LED 2 | LED 4 | Selected input |
| --- | --- | --- | --- |
| On | Off | Off | 1 |
| Off | On | Off | 2 |
| On | On | Off | 3 |
| Off | Off | On | 4 |
| On | Off | On | 5 |
| Off | On | On | 6 |

Warranty

When you receive your shipment, immediately inspect the package for shipping damage.  While it is extremely rare for shipping damage to occur, if your package is damaged notify the shipping company AND the retailer of the damage within two days.  If shipping insurance has been purchased, you will be reimbursed by the shipping company for the damaged item.  However, it is your responsibility to notify both parties within two days of receiving the damaged item.

Video Storm LLC products are covered by our manufacture’s warranty.   Our warranty covers parts and labor for 3 years following purchase.  In the unlikely event you receive an item that was not damaged in shipping but is defective please contact support@video-storm.com and we will repair or replace the item promptly.